## Slide 1: Chapter 1 Computer System Overview
Operating Systems: Internals and Design Principles, 6/E William Stallings

## Slide 2: Operating System
Exploits the hardware resources of one or more processors
Provides a set of services to system users
Manages secondary memory and I/O devices

## Slide 3: Basic Elements
Processor
  Two internal registers
    Memory address resister (MAR)
      Specifies the address for the next read or write
    Memory buffer register (MBR)
      Contains data written into memory or receives data read from memory

## Slide 4: Basic Elements
Processor
  I/O address register
  I/O buffer register

## Slide 5: Basic Elements
Main Memory
  Volatile
  Referred to as real memory or primary memory

## Slide 6: Basic Elements
I/O Modules
  Secondary Memory Devices
  Communications equipment
  Terminals
System bus
  Communication among processors, main memory, and I/O modules

## Slide 7: Computer Components: Top-Level View

## Slide 8: Processor Registers
User-visible registers
  Enable programmer to minimize main memory references by optimizing register use
Control and status registers
  Used by processor to control operating of the processor
  Used by privileged OS routines to control the execution of programs

## Slide 9: User-Visible Registers
May be referenced by machine language
Available to all programs – application programs and system programs

## Slide 10: User-Visible Registers
Data
Address
  Index register: Adding an index to a base value to get the effective address
  Segment pointer: When memory is divided into segments, memory is referenced by a segment and an offset
  Stack pointer: Points to top of stack

## Slide 11: Control and Status Registers
Program counter (PC)
  Contains the address of an instruction to be fetched
Instruction register (IR)
  Contains the instruction most recently fetched
Program status word (PSW)
  Contains status information

## Slide 12: Control and Status Registers
Condition codes or flags
  Bits set by processor hardware as a result of operations
  Example
    Positive, negative, zero, or overflow result

## Slide 13: Instruction Execution
Two steps
  Processor reads (fetches) instructions from memory
  Processor executes each instruction

## Slide 14: Basic Instruction Cycle

## Slide 15: Instruction Fetch and Execute
The processor fetches the instruction from memory
Program counter (PC) holds address of the instruction to be fetched next
PC is incremented after each fetch

## Slide 16: Instruction Register
Fetched instruction loaded into instruction register
Categories
  Processor-memory, processor-I/O, data processing, control

## Slide 17: Characteristics of a Hypothetical Machine

## Slide 18: Example of Program Execution

## Slide 19: Interrupts
Interrupt the normal sequencing of the processor
Most I/O devices are slower than the processor
  Processor must pause to wait for device

## Slide 20: Classes of Interrupts

## Slide 21: Program Flow of Control

## Slide 22: Program Flow of Control

## Slide 23: Program Flow of Control

## Slide 24: Interrupt Stage
Processor checks for interrupts
If interrupt
  Suspend execution of program
  Execute interrupt-handler routine

## Slide 25: Transfer of Control via Interrupts

## Slide 26: Instruction Cycle with Interrupts

## Slide 27: Program Timing: Short I/O Wait

## Slide 28: Program Timing: Long I/O Wait

## Slide 29: Simple Interrupt Processing

## Slide 30: Changes in Memory and Registers for an Interrupt

## Slide 31: Changes in Memory and Registers for an Interrupt

## Slide 32: Sequential Interrupt Processing

## Slide 33: Nested Interrupt Processing

## Slide 34: Multiprogramming
Processor has more than one program to execute
The sequence in which programs are executed depend on their relative priority and whether they are waiting for I/O
After an interrupt handler completes, control may not return to the program that was executing at the time of the interrupt

## Slide 35: Memory Hierarchy
Faster access time, greater cost per bit
Greater capacity, smaller cost per bit
Greater capacity, slower access speed

## Slide 36: The Memory Hierarchy

## Slide 37: Going Down the Hierarchy
Decreasing cost per bit
Increasing capacity
Increasing access time
Decreasing frequency of access to the memory by the processor

## Slide 38: Secondary Memory
Auxiliary memory
External
Nonvolatile
Used to store program and data files

## Slide 39: Cache Memory
Processor speed faster than memory access speed
Exploit the principle of locality with a small fast memory

## Slide 40: Cache and Main Memory

## Slide 41: Cache Principles
Contains copy of a portion of main memory
Processor first checks cache
If desired data item not found, relevant block of memory read into cache
Because of locality of reference, it is likely that future memory references are in that block

## Slide 42: Cache/Main-Memory Structure

## Slide 43: Cache Read Operation

## Slide 44: Cache Principles
Cache size
  Even small caches have significant impact on performance
Block size
  The unit of data exchanged between cache and main memory
  Larger block size yields more hits until probability of using newly fetched data becomes less than the probability of reusing data that have to be moved out of cache

## Slide 45: Cache Principles
Mapping function
  Determines which cache location the block will occupy
Replacement algorithm
  Chooses which block to replace
  Least-recently-used (LRU) algorithm

## Slide 46: Cache Principles
Write policy
  Dictates when the memory write operation takes place
  Can occur every time the block is updated
  Can occur when the block is replaced
    Minimize write operations
    Leave main memory in an obsolete state

## Slide 47: Programmed I/O
I/O module performs the action, not the processor
Sets the appropriate bits in the I/O status register
No interrupts occur
Processor checks status until operation is complete

## Slide 48: Interrupt-Driven I/O
Processor is interrupted when I/O module ready to exchange data
Processor saves context of program executing and begins executing interrupt-handler

## Slide 49: Interrupt-Driven I/O
No needless waiting
Consumes a lot of processor time because every word read or written passes through the processor

## Slide 50: Direct Memory Access
Transfers a block of data directly to or from memory
An interrupt is sent when the transfer is complete
More efficient